# 深圳市艾科姆斯电子有限公司

SHENZHEN IKLMS ELECTRONIC CO.,LTD

APPROVAL SHEET

CUSTOMER NAME:

CUSTOMER PART:

DESCRIPTION  :     BUZZER

EASTERN PART :     IKB0402T-SMD

| VENDOR |  | CUSTOMER |
| --- | --- | --- |
| CHECKED BY | APPROVED BY |  | COUNTERSIGN |
| 何仁梅 | 赵远云 |  |  |
| 2019-2-25 | 2019-2-25 |  |  |

公司地址：深圳市宝安区新桥街道上寮社区岗仔路6号贵达商厦405室

ADDRESS：405 room,GuiDa businessBuilding ,6th GangZai road I,ShangLiao commity,

XinQiao Subdistrict ,BaoAn District,Shenzhen City

TEL ：      +86-0755-23571160   18926019259

一. SCOPE 适用范围

This specification applies magnetic buzzer IKB4020T-SMD

二. SPECIFICATION规格

TEST CONDITION测试条件

Standard test condition: temp(+5℃～+35℃)、humidity(45～85％)、Air pressure(860～1060mbar).

标准测试条件：温度+5℃～+35℃、湿度45～85％、气压860～1060mbar。

Basic test condition: temp(25±2℃)、humidity(60～70％)、Air pressure(860～1060mbar).

基本测试条件：温度25±2℃、湿度60～70％、气压860～1060mbar。

| NO | Parameter | Specification | Unit | Condition |
| --- | --- | --- | --- | --- |
| 1 | Operating Voltage 操作电压 | 2.0-4.0 | V | - |
| 2 | Rated Voltage 额定电压 | 3.0 | V | - |
| 3 | Resonant Frequency 谐振频率 | 4000 | Hz | Applying rated voltage, standard test Condition 应用于额定电压，标准测试条件 |
| 4 | Max Rated Current 最大电流 | 90 | mA |  |
| 5 | Min Sound output(10cm) 最小声压(10cm) | 70 | dB | Distance at 10cm(A-weight free air).Applying rated voltage, standard test condition 应用于10 厘米距离，额定电压，标准测试条件 |
| 6 | Coil Resistance | 17±3 | Ω | - |
| 7 | Response time 响应时间 | - | mS | Lowest operating voltage |
| 8 | Operating Temperature 操作温度 | -20-+70 | ℃ | - |
| 9 | Storage Temperature 储存温度 | -30-+80 | ℃ | - |
| 10 | Dimension尺寸 | 4.0×4.0×2.0 | mm | 请参照外观尺寸图 See attached drawing |
| 11 | Material材质 | LCP |  | - |
| 12 | Weight重量 | 1.0 | g | - |

## 三. DIMENSIONS  尺寸图

四. RSLIABILITY TEST 性耐性试验

| No. | Item | TEST CONDITION AND REQUIREMENT | Condition standard |
| --- | --- | --- | --- |
| 1 | High Temperature Test高温试验 | After being placed in a chamber at +85℃ for 96 hours. 置于+85℃环境中96 小时。 | After the test the part shall meet specifications without any degradation in appearance and performance except SPL after 4 hours at +25℃。The SPL shall be 85 dB or More. 经测试后，静置于+25℃环境中4 小时后，单体除声压外，外观及电气特性须符合规格，输出声压为85 dB 以上。 Wave soldering temperature 265℃±5℃ and soldering time 3 to 5seconds 可承受波峰焊焊接温度265℃±5℃，焊接时间3-5秒。 |
| 2 | Low Temperature Test低温试验 | After being placed in a chamber at -40℃ for 96 hours. 置于-30℃环境中96 小时。 |  |
| 3 | Temperature Shock Test 温度冲击试验 | The part shall be subjected to 10 cycles, one cycle shall consist of.单体承受热冲击循环试验10 次，循环内容如图所示。 |  |
| 4 | Temperature Cycle Test 温度循环试验 | The part shall be subjected to 10 cycles, one cycle shall consist of.单体承受温度/湿度循环试验10 次，循环内容如图所示。 |  |
| 5 | Operating life test 寿命测试 | Ordinary temperature/室温寿命测试 The part shall be subjected to 1000 hours at room temperature (+25±10℃)with 12V. 在室温(+25±10℃)下，输入12V，连续操作1000 小时。 2. High temperature The part shall be subjected to 500 hours at +70℃ with 12V. 在+70℃环境下，输入12V，连续操作500 小时。 3. Low temperature The part shall be subjected to 500 hours at -30℃ with 12V. 在-30℃环境下，输入12V，连续操作500 小时。 |  |
| 6 | Terminal Mechanical Strength 端子强度 | The part shall be more than 10N on the direction of terminal for 10±1seconds . 沿端子轴向方向对单体施以10N 拉力 10±1 秒。 | No damage and cutting off端子不松动、不脱落 |
| 7 | Vibration 振动试验 | The part shall be subjected to a vibration cycle of 10Hz to 55Hz to10Hz in a period of 1 minute. Total peak amplitude shall be 1.52mm. The vibration test shall consist of 2 hours per axis in each three axes(X, Y, Z), total 6 hours. 振幅1.52mm，频率10Hz-55Hz-10Hz，时间1 分钟。X，Y，Z 三 个方向各2 小时，共6 小时。 | After the test the part shall meet specifications without any damage in appearance and performance except SPL shall be 85dB or more. 经试验后，单体除声压外，外观及电气特性须符合格。输出声压85dB 以上。 |
| 8 | Drop test 落下试验 | The part only shall be dropped from a height of 75cm onto a 40mm Thick wooden board 3 times in 3 axes(X, Y, Z). 单体从75 厘米高处，X，Y，Z 三个方向各三次，落于40mm 厚的 木板上。 |  |

五. MEASUREMENT SYSTEM测量系统

The oscillation frequency, current consumption and sound pressure are measured by the

measuring instruments shown below(Recommend Driving Circuit)

振荡频率、电流消耗和声压由测量仪器如下所示（推荐驱动电路）

In the measuring test, buzzer is placed as follows:

在测量测试中，蜂鸣器的位置如下

六.Soldering Condition焊接条件

Guaranteed Maximum Reflow Condition 极限回流条件 Ambient temperature NOTE : After the first reflow, the second reflow is tested on keeping MIC the usual temperature.第一次回流焊后，待产品温度恢复常温再进行第二次回流焊.

七. PACKING STANDARD 包装规格